Introduction to VLSI
Lab 4
By:
Rebecca Curtis
Kancy Robinson
David Zemon

# AND
## Layout

## Specifications
Total Area: A = 4.5 μm x 12.465 μm = 56.093 μm ^ 2
Power Consumption: P = 40 mA cdot 2.2 V + 31 mA cdot 2.2 V = 75 mW
## LVS
Compiling Diva LVS rules...

    Net-list summary for /tmp/davidzGit/project/and/LVS/layout/netlist
       count
7	nets
5	terminals
3	pmos
3	nmos

    Net-list summary for /tmp/davidzGit/project/and/LVS/schematic/netlist
       count
7	nets
5	terminals
3	pmos
3	nmos

    Terminal correspondence points
    N5 N3 A
    N4 N2 B
    N3 N5 F
    N2 N1 gnd!
    N6 N0 vdd!

Devices in the netlist but not in the rules:
        pcapacitor
Devices in the rules but not in the netlist:
        cap nfet pfet nmos4 pmos4

The net-lists match.

    layout schematic
instances
un-matched	0	0
rewired	0	0
size errors	0	0
pruned	0	0
active	6	6
total	6	6

 nets
un-matched	0	0
merged	0	0
pruned	0	0
active	7	7
total	7	7

terminals
un-matched	0	0
matched but
different type	1	1
total	5	5
# NAND
## Layout

## Specifications
Total Area: A = 4.86 μm x 9.0 μm = 43.74 μm^2
Power consumption: P = 334.3 μA cdot 1.8 V + 41.31 μA cdot 1.8 V = 676.098 mW
## LVS
Compiling Diva LVS rules...

    Net-list summary for /tmp/davidzGit/project/nand/LVS/layout/netlist
       count
6	nets
5	terminals
2	pmos
2	nmos

    Net-list summary for /tmp/davidzGit/project/nand/LVS/schematic/netlist
       count
6	nets
5	terminals
2	pmos
2	nmos

    Terminal correspondence points
    N4 N7 A
    N3 N2 B
    N2 N6 F
    N1 N1 gnd!
    N5 N0 vdd!

Devices in the netlist but not in the rules:
        pcapacitor
Devices in the rules but not in the netlist:
        cap nfet pfet nmos4 pmos4

The net-lists match.

    layout schematic
instances
un-matched	0	0
rewired	0	0
size errors	0	0
pruned	0	0
active	4	4
total	4	4

 nets
un-matched	0	0
merged	0	0
pruned	0	0
active	6	6
total	6	6

terminals
un-matched	0	0
matched but
different type	0	0
total	5	5
# OR
## Layout

## Specifications
Total Area: A = 4.545 μm x 11.475 μm = 52.154 μm^2
Power Consumption: P = 89.97 μA cdot 1.8 V + 560.97 μA cdot 1.8 V = 1,171.692 mW
## LVS
Compiling Diva LVS rules...

    Net-list summary for /tmp/davidzGit/project/or/LVS/layout/netlist
       count
7	nets
5	terminals
3	pmos
3	nmos

    Net-list summary for /tmp/davidzGit/project/or/LVS/schematic/netlist
       count
7	nets
5	terminals
3	pmos
3	nmos

    Terminal correspondence points
    N5 N2 A
    N4 N5 B
    N3 N3 F
    N2 N0 gnd!
    N6 N1 vdd!

Devices in the rules but not in the netlist:
        cap nfet pfet nmos4 pmos4

The net-lists match.

    layout schematic
instances
un-matched	0	0
rewired	0	0
size errors	0	0
pruned	0	0
active	6	6
total	6	6

 nets
un-matched	0	0
merged	0	0
pruned	0	0
active	7	7
total	7	7

terminals
un-matched	0	0
matched but
different type	0	0
total	5	5
# NOR
## Layout:

## Specifications
Total Area: A = 5.265 μm x 7.245 μm = 38.145 μm^2
Power Consumption: P = 532.08 μA cdot 1.8 V + 87.703 μA cdot 1.8 V = 1,115.609 mW
## LVS
Compiling Diva LVS rules...

    Net-list summary for /tmp/davidzGit/project/nor/LVS/layout/netlist
       count
6	nets
5	terminals
2	pmos
2	nmos

    Net-list summary for /tmp/davidzGit/project/nor/LVS/schematic/netlist
       count
6	nets
5	terminals
2	pmos
2	nmos

    Terminal correspondence points
    N4 N7 A
    N3 N5 B
    N2 N2 F
    N1 N1 gnd!
    N5 N0 vdd!

Devices in the netlist but not in the rules:
        pcapacitor
Devices in the rules but not in the netlist:
        cap nfet pfet nmos4 pmos4

The net-lists match.

    layout schematic
instances
un-matched	0	0
rewired	0	0
size errors	0	0
pruned	0	0
active	4	4
total	4	4

 nets
un-matched	0	0
merged	0	0
pruned	0	0
active	6	6
total	6	6

terminals
un-matched	0	0
matched but
different type	0	0
total	5	5
# XNOR
## Layout

## Specifications
Total Area: A = 12.825 μm x 33.795 μm = 433.421 μm^2
Power Consumption: P = 665.82 μA cdot 1.8 V = 1,198.476 mW
## LVS
Compiling Diva LVS rules...

    Net-list summary for /tmp/davidzGit/project/xnor/LVS/layout/netlist
       count
16	nets
5	terminals
12	pmos
12	nmos

    Net-list summary for /tmp/davidzGit/project/xnor/LVS/schematic/netlist
       count
16	nets
5	terminals
12	pmos
12	nmos

    Terminal correspondence points
    N14 N3 A
    N13 N5 B
    N12 N4 F
    N11 N0 gnd!
    N15 N1 vdd!

Devices in the netlist but not in the rules:
        pcapacitor
Devices in the rules but not in the netlist:
        cap nfet pfet nmos4 pmos4

The net-lists match.

    layout schematic
instances
un-matched	0	0
rewired	0	0
size errors	0	0
pruned	0	0
active	24	24
total	24	24

 nets
un-matched	0	0
merged	0	0
pruned	0	0
active	16	16
total	16	16

terminals
un-matched	0	0
matched but
different type	0	0
total	5	5
# XOR
## Layout

## Specifications
Total Area: 34.11 μm x 12.375 μm = 422.111 μm^2
Power Consumption: P = 666.48 μA cdot 1.8 V = 1,199.664 μW
## LVS
Compiling Diva LVS rules...

    Net-list summary for /tmp/davidzGit/project/xor/LVS/layout/netlist
       count
15	nets
5	terminals
11	pmos
11	nmos

    Net-list summary for /tmp/davidzGit/project/xor/LVS/schematic/netlist
       count
15	nets
5	terminals
11	pmos
11	nmos

    Terminal correspondence points
    N13 N6 A
    N12 N7 B
    N11 N3 F
    N10 N1 gnd!
    N14 N0 vdd!

Devices in the netlist but not in the rules:
        pcapacitor
Devices in the rules but not in the netlist:
        cap nfet pfet nmos4 pmos4

The net-lists match.

    layout schematic
instances
un-matched	0	0
rewired	0	0
size errors	0	0
pruned	0	0
active	22	22
total	22	22

 nets
un-matched	0	0
merged	0	0
pruned	0	0
active	15	15
total	15	15

terminals
un-matched	0	0
matched but
different type	0	0
total	5	5
# 4-Input AND
## Layout

## Specifications
Total Area: A = 5.49 μm x 56.385 μm = 309.554 μm^2
Power Consumption: P = 343.76 μA cdot 1.8 V + 359.4 μA cdot 1.8 V + 349.56 μA cdot 1.8 V = 1,959.3432 μW
## LVS
Compiling Diva LVS rules...

    Net-list summary for /tmp/davidzGit/project/4bit_and/LVS/layout/netlist
       count
22	nets
14	terminals
12	pmos
12	nmos

    Net-list summary for /tmp/davidzGit/project/4bit_and/LVS/schematic/netlist
       count
22	nets
14	terminals
12	pmos
12	nmos

    Terminal correspondence points
    N15 N10 A<0>
    N13 N12 A<1>
    N11 N13 A<2>
    N8 N11 A<3>
    N20 N6 B<0>
    N18 N8 B<1>
    N17 N9 B<2>
    N16 N7 B<3>
    N12 N3 F<0>
    N9 N2 F<1>
    N21 N4 F<2>
    N19 N5 F<3>
    N10 N1 gnd!
    N14 N0 vdd!

Devices in the netlist but not in the rules:
        pcapacitor
Devices in the rules but not in the netlist:
        cap nfet pfet nmos4 pmos4

The net-lists match.

    layout schematic
instances
un-matched	0	0
rewired	0	0
size errors	0	0
pruned	0	0
active	24	24
total	24	24

 nets
un-matched	0	0
merged	0	0
pruned	0	0
active	22	22
total	22	22

terminals
un-matched	0	0
matched but
different type	0	0
total	14	14
## Post Layout Simulation

# 4-Input OR
## Layout

## Specifications
Total Area: A = 4.54 μm x 37.035 μm = 168.139 μm^2
Power Consumption: P = -7.835 μA cdot 1.8 V + 778.04 uA cdot 1.8 V + 776.5 μA cdot 1.8 V = 2,785.572 μW
## LVS
Compiling Diva LVS rules...

    Net-list summary for /tmp/davidzGit/project/4bit_or/LVS/layout/netlist
       count
22	nets
14	terminals
12	pmos
12	nmos

    Net-list summary for /tmp/davidzGit/project/4bit_or/LVS/schematic/netlist
       count
22	nets
14	terminals
12	pmos
12	nmos

    Terminal correspondence points
    N15 N8 A<0>
    N13 N9 A<1>
    N11 N10 A<2>
    N8 N3 A<3>
    N20 N11 B<0>
    N18 N4 B<1>
    N17 N5 B<2>
    N16 N12 B<3>
    N12 N7 F<0>
    N9 N13 F<1>
    N21 N2 F<2>
    N19 N6 F<3>
    N10 N0 gnd!
    N14 N1 vdd!

Devices in the netlist but not in the rules:
        pcapacitor
Devices in the rules but not in the netlist:
        cap nfet pfet nmos4 pmos4

The net-lists match.

    layout schematic
instances
un-matched	0	0
rewired	0	0
size errors	0	0
pruned	0	0
active	24	24
total	24	24

 nets
un-matched	0	0
merged	0	0
pruned	0	0
active	22	22
total	22	22

terminals
un-matched	0	0
matched but
different type	0	0
total	14	14
## Post Layout Simulation

# 4-Input XNOR
## Layout

## Specifications
Total Area: A = 38.07 μm x 64.53 μm = 2,456.657 μm^2
Power Consumption: P = 712.66 μA cdot 1.8 V + 626.39 μA cdot 1.8 V + 604.03 μA cdot 1.8 V + 665.62 μA cdot 1.8 V = 4,695.66 μW
## LVS
Compiling Diva LVS rules...

    Net-list summary for /tmp/davidzGit/project/4b_xnor/LVS/layout/netlist
       count
58	nets
14	terminals
48	pmos
48	nmos

    Net-list summary for /tmp/davidzGit/project/4b_xnor/LVS/schematic/netlist
       count
58	nets
14	terminals
48	pmos
48	nmos

    Terminal correspondence points
    N50 N2 A<0>
    N49 N3 A<1>
    N47 N4 A<2>
    N44 N5 A<3>
    N56 N6 B<0>
    N54 N7 B<1>
    N53 N8 B<2>
    N52 N9 B<3>
    N48 N10 F<0>
    N45 N11 F<1>
    N57 N12 F<2>
    N55 N13 F<3>
    N46 N0 gnd!
    N51 N1 vdd!

Devices in the netlist but not in the rules:
        pcapacitor
Devices in the rules but not in the netlist:
        cap nfet pfet nmos4 pmos4

The net-lists match.

    layout schematic
instances
un-matched	0	0
rewired	0	0
size errors	0	0
pruned	0	0
active	96	96
total	96	96

 nets
un-matched	0	0
merged	0	0
pruned	0	0
active	58	58
total	58	58

terminals
un-matched	0	0
matched but
different type	0	0
total	14	14
## Post Layout Simulation

# 4-Input XOR
## Layout

## Specifications
Total Area: A = 33.975 μm x 59.04 μm = 2,005.884 μm^2
Power Consumption: P = 602.94 μA cdot 1.8 V = 1,085.292 μW
## LVS
Compiling Diva LVS rules...

    Net-list summary for /tmp/davidzGit/project/4bit_xor/LVS/layout/netlist
       count
54	nets
14	terminals
44	pmos
44	nmos

    Net-list summary for /tmp/davidzGit/project/4bit_xor/LVS/schematic/netlist
       count
54	nets
14	terminals
44	pmos
44	nmos

    Terminal correspondence points
    N46 N3 A<0>
    N45 N4 A<1>
    N43 N2 A<2>
    N40 N13 A<3>
    N52 N8 B<0>
    N50 N7 B<1>
    N49 N6 B<2>
    N48 N5 B<3>
    N44 N9 F<0>
    N41 N10 F<1>
    N53 N11 F<2>
    N51 N12 F<3>
    N42 N1 gnd!
    N47 N0 vdd!

Devices in the netlist but not in the rules:
        pcapacitor
Devices in the rules but not in the netlist:
        cap nfet pfet nmos4 pmos4

The net-lists match.

    layout schematic
instances
un-matched	0	0
rewired	0	0
size errors	0	0
pruned	0	0
active	88	88
total	88	88

 nets
un-matched	0	0
merged	0	0
pruned	0	0
active	54	54
total	54	54

terminals
un-matched	0	0
matched but
different type	0	0
total	14	14
## Post Layout Simulation

# 1-bit Full Adder
## Layout

## Specifications
Total Area: A = 54.855 μm x 31.95 μm = 1752.617 μm^2
Power Consumption:
## LVS
Compiling Diva LVS rules...

    Net-list summary for /tmp/davidzGit/project/1b_fullAdder/LVS/layout/netlist
       count
36	nets
5	terminals
31	pmos
31	nmos

    Net-list summary for /tmp/davidzGit/project/1b_fullAdder/LVS/schematic/netlist
       count
36	nets
7	terminals
31	pmos
31	nmos

    Terminal correspondence points
    N35 N2 A
    N34 N9 B
    N33 N4 Ci
    N32 N6 Co
    N31 N8 S

Devices in the netlist but not in the rules:
        pcapacitor
Devices in the rules but not in the netlist:
        cap nfet pfet nmos4 pmos4

The net-lists match.

    layout schematic
instances
un-matched	0	0
rewired	0	0
size errors	0	0
pruned	0	0
active	62	62
total	62	62

 nets
un-matched	0	0
merged	0	0
pruned	0	0
active	36	36
total	36	36

terminals
un-matched	0	0
matched but
different type	0	0
total	5	7
## Post Layout Simulation
# 4-bit Adder/Subtracter
## Layout

## Specifications
Total Area: A = 217.395 μm x 149.31 μm = 32,459.247 μm^2
Power Consumption:
## LVS
Compiling Diva LVS rules...

    Net-list summary for /tmp/davidzGit/project/4b_adder_subtractor/LVS/layout/netlist
       count
183	nets
17	terminals
171	pmos
171	nmos

    Net-list summary for /tmp/davidzGit/project/4b_adder_subtractor/LVS/schematic/netlist
       count
183	nets
17	terminals
171	pmos
171	nmos

    Terminal correspondence points
    N177 N5 A<0>
    N173 N4 A<1>
    N169 N6 A<2>
    N166 N7 A<3>
    N182 N8 B<0>
    N181 N9 B<1>
    N180 N10 B<2>
    N179 N11 B<3>
    N175 N3 Ci
    N172 N21 Co
    N178 N12 S<0>
    N174 N13 S<1>
    N171 N14 S<2>
    N168 N15 S<3>
    N167 N1 gnd!
    N170 N24 op
    N176 N0 vdd!

Devices in the netlist but not in the rules:
        pcapacitor
Devices in the rules but not in the netlist:
        cap nfet pfet nmos4 pmos4

The net-lists match.

    layout schematic
instances
un-matched	0	0
rewired	0	0
size errors	0	0
pruned	0	0
active	342	342
total	342	342

 nets
un-matched	0	0
merged	0	0
pruned	0	0
active	183	183
total	183	183

terminals
un-matched	0	0
matched but
different type	0	0
total	17	17
## Post Layout Simulation